## Slide 1: Overview of occupant comfort vs building energy use analysis
CSIRO ENERGY
Dr Mark Goldsworthy| Researcher
February 2019

## Slide 2: Motivations
  The National Construction Code [1] specifies minimum energy efficiency requirements for all new buildings.
  In the majority of cases compliance is demonstrated using a theoretical Star Rating calculation that assumes frequent a/c usage [2].
  Actual usage is often significantly different from these assumptions [3-7].
  As a result the regulation;
      may be unduly restrictive and/or,
      may led to perverse energy, or comfort outcomes
      (i.e. buildings that are more uncomfortable or less energy efficient factoring in how occupants actually use the building)

## Slide 3: Target outcome
  Understand the trade-off between occupant comfort in a building that is largely unconditioned, and energy use in the same building when it is conditioned.
  In particular:
        Building parameters that benefit both comfort and energy use versus those that lead to opposing effects.
        The magnitude of the effect of different parameters.
        Variation across Australian climates.

## Slide 4: Analysis approach
  Simulation model of building physics + reverse cycle a/c + BOM weather data
      12 different building parameters varied
      Annual simulations of 2000 buildings at 83 representative weather station sites.
      Linked satellite irradiance data with ground station measurements
      Choose 5 most complete years of weather data from 1997-2017.
      For each case, 2 simulations:
        Unconditioned (free-running) measure ‘discomfort’
        Air-conditioned measure energy use
      Calculate annual averages over 5 simulated years for each building/site combination
      Statistical analysis to assess significant effects of building parameters

## Slide 5: Analysis approach
Building parameters considered:
Notionally one ‘above average’ parameter value and one ‘below average’ value.
Variable | Parameter values
Thermal capacitance (ratio of air thermal capacitance) | 5x, 15x
Infiltration rate | 0.5,2.0 a/hr
Internal load multiplier | 0.5x, 1.0x (see Figure 3)
Building aspect ratio | 1:1, 2:1
Orientation (degrees from Nth) | 0, 45, 90, 135, 180, 225, 270, 315°
Ceiling insulation | None, R3
Roof solar absorptivity | 0.3, 0.9
Wall insulation | None, R2
Wall construction (thermal mass) | Light (weatherboard), Medium (brick veneer), Heavy (double-brick)
Wall solar absorptivity | 0.3, 0.75
Window area | 2.5m², 5m²
Window type | Single glazed, double glazed

## Slide 6: Results
Note: positive mean scale parameter means the parameter value to the right in the previous table
(generally the numerically higher value) leads to a higher energy use or discomfort.

## Slide 7: Results
Parameter | Qualitative mean effect size | Summary of annual mean effect
Ceiling insulation | Large | Ceiling insulation lowers energy use for all climates but improves comfort only for heating dominated climates. The climate of Sydney represents an approximate division between these two groupings.
Natural infiltration | Large | Higher infiltration increases energy use on average for all climates but improves comfort in almost all climates except those that are strongly heating dominated. Comfort improvement is greatest for cooling dominated climates while the energy penalty is least for climates with moderating coastal breezes.
Orientation (window) | Large | South facing window orientation leads to lower energy use and improved comfort for all non-alpine climates. In general, easterly orientations are better than westerly, with the exception of a small number of climates where easterly and westerly were similar.
Wall construction | Moderate-Large | Double brick wall construction lowers energy use and improves comfort for non-tropical climates.
Roof absorptivity | Moderate-large | Darker coloured roofs lower energy use and improve comfort for heating dominated climates and have the opposite effect for cooling dominated climates. The climate of Hobart represents the approximate division between these two groupings.
Wall insulation | Moderate-large | Wall insulation lowers energy use. Wall insulation reduces comfort for all climates excluding alpine and sub-alpine.
Internal load | Moderate-large | Higher internal load lowers energy use and improves comfort for heating dominated climates and has the opposite effect for cooling dominated climates. The climate of Melbourne represents the approximate division between these two groupings.
Wall absorptivity | Moderate | Darker coloured external walls lower energy use and improve comfort for heating dominated climates and have the opposite effect for cooling dominated climates. The climate of Hobart represents the approximate division between these two groupings.
Internal capacitance | Small | Higher capacitance lowers energy use and improves comfort. The effect is relatively small.
Window type | Small* | Double glazed (low solar gain) windows lower energy use for all climates with negligible change to comfort.
*Although the mean (averaged) effect is small across all cases, the effect can be large, for example, for windows with certain orientations.

## Slide 8: Summary
  Some building parameters do lead to universally lower energy use and better comfort. However, several show opposing effects.
  This brings into question the use of a conditioned building alone as the gold standard for design. In reality there is a design trade-off;
      The most efficient building is the one in which occupants feel comfortable without any air-conditioning!
  Incorporating both a comfort metric and an energy use metric, together with more realistic models of a/c use, would lead to improved building designs, lower energy use and better outcomes for occupants.

## Slide 9: Potential next steps
Understanding the extent to which different buildings create comfortable ‘liveable’ conditions for occupants (either with or without a/c).
Simulation of actual building designs. Accounting for;
  both comfort and energy use
  realistic a/c usage behaviours
Better understanding a/c usage behaviours

## Slide 10: References
[1] Australian Building Codes Board. National Construction Code, Volume 2. Canberra : ABCB, 2016
[2] NatHERS National Administrator. Nationwide house energy rating scheme - software accreditation protocol. Canberra : DCCEE, 2012.
[3] Thermal comfort and occupant responses during summer in a low to middle income housing development in South Australia. Soebarto, V. and Bennetts, H. s.l. : Elsevier, 2014, Building and Environment, Vol. 75, pp. 19-29.
[4] Strategic Insights. Queensland Household Energy Survey 2013. Brisbane : Colmar Brunton, 2014.
[5] Towards a residential air-conditioner usage behaviour model for Australia. Goldsworthy, M.J. s.l. : Elsevier, Energy and Buildings, Vol. Submitted manuscript.
[6] House energy rating schemes and low energy dwellings: the impact of occupant behaviours in Australia. Daniel, L., Soebarto, V. and Williamson, T. s.l. : Elsevier, 2015, Energy and Buildings, Vol. 88, pp. 34-44.
[7] Energy consumption of 100 Australia residential air conditioners. Law, A., et al. s.l. : AIRAH, November 2014, Ecolibrium.

## Slide 11: Thank you
ENERGY
  MARK GOLDSWORTHY
  RESEARCHER
    t +61 2 4960 6112
    e mark.goldsworthy@csiro.au
    w www.csiro.au/
ENERGY