## Slide 1: Energy consumption
Peter Toscas | Research Group Leader
25 January 2019
The effect of building age

## Slide 2: Introduction
Motivation
Data used
Methodology adopted
Results
Future work

## Slide 3: Why undertake this work?
A number of changes to building codes and standards in Australia
  2003 – minimum energy efficiency regulations introduced
  2006 – Class 1a residential buildings to be 5-stars
  2010 – Class 1a residential buildings to be 6-stars
  Building energy efficiency requirements have changed as a result
  Productivity Commission (2005): “There is considerable uncertainty about the extent to which building standards have reduced energy consumption and emissions.”
  Aim of work: Is it possible to identify if changes in residential building energy requirements have resulted in detectable shifts in energy usage?
Notes: Class 1a – “a detached house or one of a group of two or more dwellings separated by a fire resisting wall, including a row house, terrace house, town house or villa unit.”

## Slide 4: Data – Australia wide
Three data sets linked together
  Building Exposure data from Geoscience Australia (also used for the SEQ)
    This data set contains information on:
      Number of buildings built at different times
      The footprint size of buildings
      The type of building material used for walls and roofs of buildings
      Socio-economic variables.
  Meteorological readings from local weather stations across Australia
    This data set was used to derive a number of meteorological variables:
    Apparent temperature (incorporates temperature and humidity information)
    “Heating” and “cooling” degree days (higher values mean more “heating” or “cooling” days than those regions with lower values).
  ABS 4670.0 Household Energy Consumption Survey for non-generating residential meters across Australia (except Northern Territory)
      Annual data for 2010 – 2012
      Data at SA2 level
      SA2s assigned to one of 7 climate zones:
        High humid summer, warm winter
        Warm humid summer, mild winter
        Hot dry summer, warm winter
        Hot dry summer, cool winter
        Warm temperature
        Mild temperature
        Cool temperature

## Slide 5: Data – Australia wide (continued)
Why use the Australia wide annual energy consumption data?
  Covers most of Australia so offers the opportunity to check if differences exist under different climatic conditions
Limitations with the data used:
  Yearly data – so not able to test for differences at finer temporal scales
  Only 3 years worth of yearly data so not able to check for trends over time
  SA2 level data – not really able to test at the individual building level

## Slide 6: Methodology – Australia wide
Linear mixed effects modelling analysis undertaken to analyse the data
  A response variable (e.g. energy consumption) is related to explanatory variables which are tested to see if they help explain a “significant amount” of variation in the response variable
  The linear mixed effects allows some variables to have random coefficients:
    Each SA2 can have different intercept
    No trend or seasonal effects included as not enough time points in the data
  Twist: Many explanatory variables are compositional in nature. For example, they can represent the proportion of separate houses, proportion of semi-detached dwellings and the proportion of flats/units
  The linear mixed effects analysis respects the compositional nature of many of the explanatory variables.

## Slide 7: Results – Australia wide
Analysis of annual residential energy usage for the Australia wide SA2s showed that the following variables explained significant variation in the mean residential energy usage:
  Building age
  Wall type
  Roof type
  Building type floor area
  Equivalised income
  Tenure type
  Interaction between cooling degree days and climate zone

## Slide 8: Results
Three building age categories compared:
  Built before 1982
  Built from 1982 to 1996
  Built from 1997 to 2011
Buildings built from 1982 to 1996, on average, had significantly higher household average annual energy consumption than the buildings built:
  Before 1982
  From 1997 to 2011
Buildings built before 1982 had marginally lower average yearly household energy consumption than those built from 1997 to 2011

## Slide 9: Results

## Slide 10: Results
Direct comparison between buildings built from 1982 to 1996 and those built from 1997 to 2011 reveals the former group on average could use over 271 kWh more energy per year than the latter group
  At a conservative 25c/kWh, this amounts to $67.75 extra charges per year

## Slide 11: Thank you
Data61/Data-driven Enterprises Analytics
  Peter Toscas Research Group Leader
    t +61 3 9545 8054
    e peter.toscas@data61.csiro.au
    w www.data61.csiro.au