## Slide 1: Air-conditioner use prediction from interval meter data
Asia-Pacific Solar Research Conference – Sydney 2018
CSIRO ENERGY
Dr Mark Goldsworthy | Researcher
5 December 2018

## Slide 2: Context
Uptake of interval/smart electricity meters steadily increasing
Victoria alone -> 40,000,000,000 data points / year
How could this data be used to provide benefit?

## Slide 3: Motivations…

## Slide 4: Motivations…
Chart: 
| Heating | Cooling | Hot water | Lighting & plug loads | Pool pump
 | 9.4848 | 126.464 | 56.9088 | 66.3936 | 56.9088

## Slide 5: Motivations…
Chart: 
| Heating | Cooling | Hot water | Lighting & plug loads | Pool pump
 | 9.4848 | 126.464 | 56.9088 | 66.3936 | 56.9088
“You could save $30 by turning on air-conditioning
1 hour later…”

## Slide 6: Motivations…
Interval electricity meter data could be used to
Understand (air-conditioner) usage behaviours and patterns
Predict (air-conditioner) use under different scenarios
(e.g. different tariff structures, technology or climate changes)
Provide feedback & advice to consumers
…

## Slide 7: Starting problem
Approximate location
Energy use (30 min)
Date & time
Model?
Air-conditioning on/off

## Slide 8: Starting problem
Approximate location
Energy use (30 min)
Date & time
Model?
Air-conditioning on/off
Only stipulation: the model should have physically meaningful parameters

## Slide 9: Model basis
= Deviation from comfortable conditions (absolute measure)
    Uses ambient temperature
    Compared to a reference level that varies by time of day
    Positive (cooling more likely), negative (heating more likely)
    Larger amplitude if recent conditions were more uncomfortable (& vice-versa)
= Relative energy consumption
    Compared to the same time of day on a mild day
- Location -> weather
- Date & time
- Energy use (30 min)
evaluated every 30 minutes

## Slide 10: Training a single house model (known data)
Training information
A/c on/off prediction
House A model
House A
Weather data

## Slide 11: Results
Gaussian Process Classification model
No predetermined function
Output is probability of a/c on/off
Trained using 400 on and off intervals
Tested with 2 years of data
Overall prediction accuracy (RMSE=9.2hrs)

## Slide 12: Example models
Gaussian Process Classification model
No predetermined function
Output is probability of a/c on/off
Trained using 400 on and off intervals
Tested with 2 years of data
Overall prediction accuracy (RMSE=9.2hrs)

## Slide 13: Generalising the model

## Slide 14: Generalising the model
Set of generic models
Model A
House A
Model B
House B
Model C
House C
Clustering
Households used to build generic models
Identification
Prediction
Households to predict a/c use
Model development
Model use

## Slide 15: Generalising the model
Clustering
i.e. building a set of representative models (143 -> 6 representative models)
  Clustering by similar behaviour
  Not essential (could just keep all 143 models)
Identification
i.e. determining which model to use for a given house
  Different approaches possible
    e.g. shape of Lt-Le space, information about occupants or dwelling
  Here using small number (i.e. 1 or 2) of known sampling points

## Slide 16: Effect of clustering (143 models -> 6 models)
Overall prediction accuracy (RMSE=27.8hrs)
Example of 30 minute prediction compared to
a/c circuit energy use

## Slide 17: Identification (i.e. choosing the model to use for a given house)
What if we could ask the household if they are using a/c 1 or just a couple of times.
How useful would this be?
When should we ask to maximise the information gained?

## Slide 18: Identification (i.e. choosing the model to use for a given house)
What if we could ask the household if they are using a/c 1 or just a couple of times.
How useful would this be?
When should we ask to maximise the information gained?
Choose a potential time to sample
Evaluate the likely predictive power based how well a yes/no answer would distinguish between the models
Decide whether to ask based on entropy minimisation

## Slide 19: Identification (i.e. choosing the model to use for a given house)
What if we could ask the household if they are using a/c 1 or just a couple of times.
How useful would this be?
When should we ask to maximise the information gained?
Choose a potential time to sample
Evaluate the likely predictive power based how well a yes/no answer would distinguish between the models
Decide whether to ask based on entropy minimisation
Only need to ask 2 or 3 times to
get significant improvement

## Slide 20: Issues
Temperature dependent loads connected to GPO’s
  -air-conditioning loads (electric heaters, portable a/c etc.)
  -non air-conditioning loads (e.g. fridge/freezer)
Temperature dependent non-air-conditioning behaviour changes
  -only an issue if energy use variation is large

## Slide 21: Conclusion & suggested next steps
Feasibility of the approach demonstrated
Acceptable accuracy depends on intended use
Suggested next steps
  Build a better set of representative models
  Separate out controlled or predictable loads (e.g. hot water)
  Refine neutral temperature (e.g. location dependent)
  Investigate use of other data for identification step
  Change from on/off status to energy use

## Slide 22: Thank you
CSIRO Energy
  Dr Mark Goldsworthy Researcher
    t +61 2 4960 6112
    e mark.goldsworthy@csiro.au
    w www.csiro.au/lorem
ENERGY
Image attributions:
Images available from the Noun Project under creative commons attribution licenses
  Computer by Esteban Sandoval from the Noun Project
  Air conditioner by Symbolon, IT from the Noun Project
  House tenant (modified) by Symbolon, IT from the Noun Project
  Electricity meter by Templet from the Noun Project
  Line graph by Vectors Market from the Noun Project
  Weather by Dinosoft Labs, PK from the Noun Project